## Slide 1
zk
SPECIAL TOPICS IN HARDWARE DESIGN · PROJECT PRESENTATION
MAY 2026
zkPHIRE
A programmable FPGA accelerator for the SumCheck bottleneck in zero-knowledge proofs.
Sammy Suliman
Jui-Teng Huang
Ashesh Kaji
BN254 · HLS · PYNQ-Z2

## Slide 2
02 / 16
zkPHIRE
ZERO-KNOWLEDGE PROOFS, IN ONE SENTENCE
Prove the claim. Hide the witness.
Prover
knows witness w
Verifier
sees only proof π
commitment, π
random challenge r
response
witness w never crosses the line
Complete
True claim → accepted by the verifier.
Sound
False claim → rejected by the verifier.
Zero knowledge
Transcript leaks nothing about witness w.

## Slide 3
03 / 16
zkPHIRE
HOW COMPUTATION BECOMES ALGEBRA
Circuits become polynomial identities.
CIRCUIT GATE
w₁
w₂
×
w₃
encode
POLYNOMIAL CONSTRAINT
qL·w₁ + qR·w₂ + qM·w₁w₂ − qO·w₃ + qC = 0
selectors q encode the gate type
Each gate → a constraint
Every gate becomes an algebraic equation that evaluates to zero on valid inputs.
Verifier checks polynomials, not traces
The verifier checks randomized polynomial claims rather than executing the full circuit.

## Slide 4
04 / 16
zkPHIRE
THE PROTOCOL KERNEL WE ACCELERATE
SumCheck shrinks a sum over 2ᵘ points into μ small checks.
ROUND 1
size 8
s₁(X₁)
fix r1
ROUND 2
size 4
s₂(X₂)
fix r2
ROUND 3
size 2
s₃(X₃)
fix r3
FINAL
size 1
f(r₁,r₂,r₃)
verifier check
sᵢ(0)+sᵢ(1) = sᵢ₋₁(rᵢ₋₁)
each round halves the table — μ rounds total, one variable fixed per round
claimed total: C = Σ_{x₁,…,xᵤ ∈ {0,1}} f(x₁, …, xᵤ)

## Slide 5
05 / 16
zkPHIRE
WHY THIS BELONGS IN A HARDWARE DESIGN CLASS
Proof generation is the bottleneck.
CPU
minutes — hours
FPGA / ASIC TARGET
orders of magnitude faster
256
bit field elements — wide modular multiplies
d + 1
univariate samples per degree-d round
2ᵘ
MLE table size — heavy memory pressure

## Slide 6
06 / 16
zkPHIRE
PAPER: ZKPHIRE — A PROGRAMMABLE ACCELERATOR FOR ZKPS
The paper's idea: programmable SumCheck for high-degree gates.
Instead of a fixed SumCheck datapath for one gate type, zkPHIRE supports arbitrary high-degree, expressive gate polynomials.
Programmability
Schedules different polynomial terms, degrees, and reuse patterns.
Locality
Tiled scratchpads reuse MLE table data across terms.
System integration
Embeds SumCheck into a HyperPlonk accelerator with MSM, SHA3, modular inverse, and forest units.

## Slide 7
07 / 16
zkPHIRE
WHAT THE HPCA PAPER REPORTS
Large speedups, small proofs, and custom gate support.
1000×+
Geomean speedup over CPU-based SumChecks across gate types.
1486×
Geomean full-system speedup over CPU for HyperPlonk.
4–5 KB
Proof sizes remain succinct while scaling to large problems.
Numbers are from the paper abstract in docs/paper/zkphire.pdf.

## Slide 8
08 / 16
zkPHIRE
OUR IMPLEMENTATION TARGET
One SumCheck round as a reusable HLS IP block.
PAIR
f[2k], f[2k+1]
read MLE pairs
EXTEND
L(z), z = 0…d
d+1 sample points
MULTIPLY
Π Lᵢ(z)
all factors per term
ACCUMULATE
s(z) = Σ Pₖ(z)
round polynomial
UPDATE
f′[k] = L(r)
halve the table
verifier challenge r feeds the next round
Programmable in HLS
Implemented as a single round, parameterizable across degree d.
Reusable as IP
Clean control interface and golden-model verified for drop-in use.

## Slide 9
09 / 16
zkPHIRE
ENGINEERING DESIGN CHOICE 1: VALIDATION-FIRST DEVELOPMENT
The golden model is the specification.
Before optimizing hardware structure, we locked down one-round behavior in a bit-exact Python reference model and made every HLS target prove that it matches.
Reference semantics
golden_sumcheck.py defines BN254 field arithmetic, round polynomial samples, challenge-based table updates, and protocol-chain invariants.
Stable regression cases
Hand-checkable deterministic examples plus randomized degree-2 through degree-6 checks catch both math and indexing mistakes.
Hardware acceptance test
C-simulation is not considered passing unless every samples[x] value and every updated[m][k] entry matches the golden output.
HLS is correct ⟺ ∀ x, m, k : samples_hls[x] = samples_gold[x] ∧ updated_hls[m,k] = updated_gold[m,k]

## Slide 10
10 / 16
zkPHIRE
ENGINEERING DESIGN CHOICE 2: IP INTERFACE CONTRACT
Control stays scalar; field tables move through memory.
The SumCheck round has tiny configuration state but large 256-bit table buffers, so the interface separates AXI-Lite control from bulk memory movement.
AXI-Lite for control
Field | Why it is scalar
degree | Sets number of MLE factors and d+1 samples.
size | Current power-of-two table length.
r | Verifier challenge for next-table update.
return | Status code for bad degree, size, or challenge.
BRAM array top
sumcheck_round_array — structured C-sim interface: tables[m][i], samples[x], updated[m][k].
m_axi DMA top
sumcheck_round_axi — flattens buffers for host: inputs at m*size+i, outputs at x and m*(size/2)+k.
Why this choice
Matches how a host launches reusable IP: configure once, stream/DMA buffers, then poll status.

## Slide 11
11 / 16
zkPHIRE
ENGINEERING DESIGN CHOICE 3: SELF-CHECKING TESTBENCHES
Testbenches check behavior, not just completion.
The HLS testbench is intentionally deterministic and element-wise, so failures point to the exact sample or updated-table entry that diverged from the golden model.
Hand-checkable cases
Case A uses x₁x₂x₃ with challenge chain (5,7,11), including edge checks for r=0 and r=1.
Composition coverage
Case B tests x₁x₂ and x₂x₃ individually, then the combined polynomial x₁x₂ + x₂x₃.
Element-wise assertions
Each run compares every sample and every next-table cell; a passing run = full IP contract matched.
1 · LOAD VECTOR
Populate 256-bit MLE tables with deterministic fixtures.
2 · RUN IP
Call the same top-level function used for synthesis.
3 · COMPARE
Check samples and updated against golden values.
4 · REPORT
Emit named PASS/FAIL; current suite: 7/7 on both targets.

## Slide 12
12 / 16
zkPHIRE
ENGINEERING DESIGN CHOICE 4: DIVIDE THE PAPER INTO HLS MODULES
We translated the SumCheck datapath into small, testable header files.
types.hpp
field type, P, limits
field_arithmetic.hpp
BN254 add / sub / mul
scratchpad.hpp
local table storage
extension_engine.hpp
pair → L(z)
product_lane.hpp
multiply factors
accumulator.hpp
sum into s(z)
update_unit.hpp
apply challenge r
src/sumcheck_top.cpp
orchestrates BRAM + m_axi top functions
Each datapath stage = a named HLS unit · small headers isolate bugs · top file composes BRAM + m_axi interfaces

## Slide 13
13 / 16
zkPHIRE
ENGINEERING DESIGN CHOICE 5: PROMPT ONE MODULE AT A TIME
We used careful AI prompting as a hardware-specification tool.
Why prompts worked
Each prompt gave the AI a role, the mathematical contract, Vitis HLS constraints, resource notes, and the exact functions to implement.
Guardrails
One header at a time, stable interfaces via types.hpp, every output validated against the golden model and C-sim testbench.
Example shown
This prompt targets field_arithmetic.hpp, which depends on types.hpp for the BN254 type and field prime.
PROMPT — field_arithmetic.hpp
Role: Expert FPGA design engineer specializing in Vitis HLS and Cryptographic Hardware.
Task: Write field_arithmetic.hpp implementing modular arithmetic for the BN254 scalar field.
Mathematical Context:
BN254 scalar prime P =
21888242871839275222246405745257275088
548364400416034343698204186575808495617
Requirements:
• Include types.hpp.
• bn254_add(a,b): (a+b) mod P — add + conditional subtract of P (save DSPs).
• bn254_sub(a,b): (a-b) mod P — add P on underflow.
• bn254_mul(a,b): (a·b) mod P — Phase 1: (ap_uint<512>(a)*b) % P. Montgomery in Phase 3.
• Mark all functions inline for hardware pipelining.

## Slide 14
14 / 16
zkPHIRE
HARDWARE BRING-UP ISSUE: PYNQ-Z2 DSP BUDGET
Functionally correct, but too DSP-heavy for the board.
Our PYNQ-Z2 C-simulation passed and timing met 100 MHz, but the board only has 220 DSPs. Direct 256-bit BN254 modular multiplication pushed implementation over that limit.
220
DSPs available on PYNQ-Z2
233
DSPs after shared-multiplier optimization
105%
DSP utilization — cannot comfortably fit on-board
What caused the issue?
The Phase 1 multiplier used ap_uint<512>(a) * b % FIELD_P — simple and bit-exact, but expensive on a small Zynq-7020.
What we tried / learned
Sharing mod_mul cut DSPs from 458 → 233 (48% reduction). Barrett made DSPs worse (683). BIND_OP impl=fabric unsupported on xc7z020.

## Slide 15
15 / 16
zkPHIRE
CONCLUSION: WHAT THE PYNQ ISSUE TAUGHT US
Montgomery multiplication is the right fix for small FPGA deployment.
The PYNQ-Z2 failure was not a SumCheck correctness problem. It was an arithmetic architecture problem: generic modular division for BN254 consumed too many DSPs.
What Montgomery changes
Operands live in the Montgomery domain. Multiplication = a 512-bit product, a reduction factor from the low 256 bits, a shift, and one conditional subtraction.
Why it helps PYNQ
Replaces the DSP-heavy % reduction with precomputed constants: R = 2^256, R² mod p, and p′ = −p⁻¹ mod R.
~60
estimated DSPs after Montgomery
<100
README target for fitting PYNQ-Z2
0
division operations in Montgomery reduction

## Slide 16
THANK YOU
Questions?
zkPHIRE SumCheck Accelerator
Protocol
One programmable SumCheck round over BN254.
Implementation
Modular Vitis HLS design with golden-model validation.
Hardware lesson
PYNQ-Z2 deployment is constrained by DSP-heavy field arithmetic.
Sammy Suliman · Jui-Teng Huang · Ashesh Kaji